The Board we are going to use:

https://www.aliexpress.com/item/Wemos-ESP8266preflashed-development-board-OLED-version-ESP8266-18650-OLED/32819513410.html?spm=a2g0s.9042311.0.0.3da24c4dJDfL18

Esp8266 Motherboard ESP8266 Mini-WiFi NodeMCU Module
18650 holder
 Battery OLED
Model:ESP-8266
Color:Black
Charging Protection:Yes
Discharge Protection:Yes
Compatible With NodeMCU
Wide Voltage Input Range: 5V~12V
Charge Current:500 mA
Size(L*W*H):102 x 30 x 20 mm
Display Size: 0.96 In

Features:
1.One AD (Analog to Digital) inputs.
2.Micro USB inputs.
3.One programmable LED (D0 = GPIO16).
4.Integrated 18650 battery charging and discharging system.
5.One switch controls whether the 18650 battery is powered or not.
6.OLED's SDA and SCL connect to the D1 pin and the D2 pin respectively.
7.The five buttons are controlled by FLASH, RSET, D5, D6, and D7 respectively.
8.The 5 Digital pins can configure the write/read/interrupt/pwm/I2C/one-wire supported separately.
9.Operation and NodeMCU consistent, adding a programmable LED, you can use GPIO16 to control, display 8266 running status and other functions. Integrated OLED (SSD1306 chip) and five button, more convenient for development.
10.The design concept originates from the open source project NodeMCU,
and the development board integrates 18650 charging and discharging systems with charging and discharging protection.
At the same time, a OLED and five directional buttons are integrated to facilitate the development.

Dimension drawings (manual measurements, with some 1-3MM errors):

GPIO to PIN Mapping
Pin Names on NodeMCU Development Kit	ESP8266 Internal GPIO Pin number
D0	GPIO16
D1	GPIO5
D2	GPIO4
D3	GPIO0
D4	GPIO2
D5	GPIO14
D6	GPIO12
D7	GPIO13
D8	GPIO15
D9/RX	GPIO3
D10/TX	GPIO1
D11/SD2	GPIO9
D12/SD3	GPIO10