# Using the Buttons and Interrupts

The Chosen board has some buttons connected as follows:
Function	PIN	GPIO
Button-Press	D5	GPIO14
Button-UP	D6	GPIO12
Button-DOWN	D7	GPIO13

To access these buttons, you could just digitally read these pins in the loop function. Or you could attache them to interrupts.
Usually attaching to interrupts is better as you may miss a button press if the loop functions takes too long running.
Interrupts: are events or conditions that stops the processor from executing the normal line or sequence of code (Setup and loop functions) into a different sequence of temporary code (another function) and then back again into the normal line of code.
Interrupts are usually tied up to a PIN on the micro controller. Even in some processors, only a couple of pins are allowed to be attached to interrupts.
Start a new project sand lets try to tie the buttons to the interrupts.
To use interrupts, you usually start in the setup function:
Setup(){
/////////////////////////////////////////////
Serial.begin(115200);
Serial.println("Started..");
// detect D5,D6 and D7 joystick button
 int interruptPinD5= D5;
 int interruptPinD6= D6;
 int interruptPinD7= D7;
//INPUT, OUTPUT, or INPUT_PULLUP
 pinMode(interruptPinD5, INPUT_PULLUP);
 pinMode(interruptPinD6, INPUT_PULLUP);
 pinMode(interruptPinD7, INPUT_PULLUP);
 //CHANGE, RISING and FALLING
 attachInterrupt(digitalPinToInterrupt(interruptPinD5), handleInterruptD5, FALLING);
 attachInterrupt(digitalPinToInterrupt(interruptPinD6), handleInterruptD6, FALLING);
 attachInterrupt(digitalPinToInterrupt(interruptPinD7), handleInterruptD7, FALLING);
 ///
}

The used built in functions:
pinMode	https://www.arduino.cc/reference/en/language/functions/digital-io/pinmode/
attachInterrupt	https://www.arduino.cc/reference/en/language/functions/external-interrupts/attachinterrupt/
DigitalPinToInterrupt	https://www.arduino.cc/reference/en/language/functions/external-interrupts/attachinterrupt/ / Same link as attachInterrupt

Then add these functions outside the setup() and loop() functions:

void handleInterruptD5() {
 Serial.print("D5:press:");
 Serial.println(D5);
}
void handleInterruptD6() {
 Serial.print("D6:up:");
 Serial.println(D6);
}
void handleInterruptD7() {
 Serial.print("D7:down:");
 Serial.println(D7);
}
In the loop function:
loop(){
Serial.println("looping");
delay(60000);
}
Compile , Upload “CTRL-U” the sketch and check the results in the Serial Monitor.